## Slide 1: Learning Resource On Software Engineering
Chapter-10
Software Reliability and Quality Management
Prepared By:
Kunal Anand, Asst. Professor
SCE, KIIT, DU, Bhubaneswar-24

## Slide 2: Chapter Outcomes:
After completing this chapter successfully, the students will be able to:
  Explain the significance of reliability in software product.
  Define software reliability.
  Compare and contrast hardware and software reliability.
  Describe different software reliability metrics.
  Identify different types of failures.
  Exaplain reliability growth modeling.
  Define software quality.
  List different quality factors.
  Distinguish between product metrics and process metrics.
  Illustrate ISO 9000
  Describe SEI CMM levels
  Compare and contrast ISO 9000 and SEI CMM

## Slide 3: Organization of this Chapter
Introduction to Software Reliability
Reliability Metrics of software products
Reliability Growth Modeling
Introduction to Software Quality
Quality Systems
ISO 9000
SEI CMM

## Slide 4: Introduction to Software Reliability
Reliability of a software product, is a concern for most users especially industry users as it is an important attribute determining the quality of the product.
Users not only want highly reliable products, but also, they want quantitative estimation of reliability before making buying decision.
It is difficult to measure reliability of a software product as the measure is an observer dependent entity. Also, several factors contributing into reliability making its measurement more difficult.

## Slide 5: Software Reliability
Formally, software reliability can be defined as the probability of the product working correctly over a given period.
Intuitively, a software product having many defects is unreliable. It is also clear that reliability of a system generally improves if the number of defects is reduced.
The reliability of a product depends not only on the number of latent errors but also on the exact location of the errors.
Again, reliability also depends on the fact that how the product is used.

## Slide 6: The 90-10 Rule
Experiments from analysis of behaviour of many programs indicate that 90% of the total execution time is spent in executing only 10% of the instructions in the program.
The most used 10% instructions is called the core of the program. Least used 90% statements, called non-core, are executed only during 10% of the total execution time.
It may not be very surprising then that removing 60% defects from least used parts would lead to only about 3% improvement to product reliability.

## Slide 7: Hardware Reliability vs Software Reliability
The reliability of hardware and software products are different in nature.
  Hardware failures mostly happen due to wear and tear in components. The faulty components must be repaired or replaced to maintain the reliability of the product. On the other hand, the software failures are latent in nature i.e., the software will continue to fail till the error is tracked down and rectified.
  When a hardware is repaired, its reliability is maintained whereas when software is repaired, its reliability may increase or decrease or remain same.

## Slide 8: Software Reliability Metrics
The reliability issue must be clearly mentioned in the SRS document.
For this purpose, some metrics are used to quantitavely express the reliability of a software product.
Following six reliability metrics can be used for the above said purpose:
  Rate of occurrence of failure (ROCOF)
  Mean time to failure (MTTF)
  Mean time to repair (MTTR)
  Mean time between failures (MTBF)
  Probability of failure on demand (POFOD)
  Availability

## Slide 9: Reliability Metrics
Rate of occurrence of failure i.e., ROCOF, measures the frequency of occurrence of unexpected behavior of the system.
  It can be obtained by observing the behavior of the system over a specified period and then calculating the total no. of failures during this interval.
Mean time to failure i.e., MTTF is the average time between two successive failures, observed over many failures.
Mean time to repair i.e., MTTR is the average time required to track the errors causing the failure and then to fix them.
Mean time between failures i.e., MTBF is the expected time duration between two successive failures. It can be obtained by combining the metrics MTTF and MTTR.
  For example, MTBF of 300 hrs. indicates that once a failure occurs, the next failure is expected at least after 300 hrs..

## Slide 10: Reliability Metrics
Probability of failure on demand i.e., POFOD measures the likelihood of the system failing when a service request is made.
  A POFOD of 0.001 means 1 out of every 1000 service requests would result in a failure.
Availability is a measure of how likely will the system be available for users over a given period.
  This is very important for such systems which are always expected to be in service and with significant repair time. e.g., Telecommunication system, OS etc.

## Slide 11: Failure classes
All reliability metrics we discussed are centred around the probability of system failures.They take no account of the consequences of failures i.e.; severity of failures may be very different.
To accurately estimate reliability of a software product, it is necessary to classify different types of failures.
  Transient failures occur only for certain inputs.
  Permanent failure occurs for all input values.
  For Recoverable failure, the system recovers with or without operator intervention.
  In Unrecoverable failures, the system may have to be restarted.
  Cosmetic failures just cause minor irritations. They do not lead to incorrect results.

## Slide 12: Reliability Growth Modelling
A reliability growth model is a mathematical model of how software reliability grows as errors are detected and repaired.
A reliability growth model can be used to predict when (or if at all) a particular level of reliability is likely to be attained. i.e., how long to test the system?
There are two main types of uncertainty in modelling reliability growth which render any reliability measurement inaccurate:
  Type 1 uncertainty: our lack of knowledge about how the system will be used, i.e., its operational profile
  Type 2 uncertainty reflects our lack of knowledge about the effect of fault removal. i.e. When we fix a fault, we are not sure if the corrections are complete and successful, and no other faults are introduced. Even if the faults are fixed properly, we do not know how much will be the improvement to inter-failure time.

## Slide 13: Reliability Growth Modelling
Step Function Model makes a basic assumption that the reliability increases by a constant amount each time an error is detected and repaired.
ROCOF
time
Assumes that all errors contribute equally to reliability growth.
Unrealistic as we already know that different errors contribute differently to reliability growth.

## Slide 14: Contd..
Jelinski and Moranda Model
  This model states that each time an error is repaired reliability does not increase by a constant amount.
  Reliability improvement due to fixing of an error assumed to be proportional to the number of errors present in the system at that time.
  Realistic for many applications, but still suffers from several shortcomings.
Littlewood and Verall’s Model
  This model allows for negative reliability growth to reflect the fact that when a repair is carried out, it may introduce additional errors.
  It also models the fact that as errors are repaired the average improvement in reliability per repair decreases.
Note: There is no universally applicable reliability growth model. Reliability growth is not independent of application. Take the model which most suitable fits the data.

## Slide 15: Software Quality
A quality product is defined in terms of its “fitness of purpose”. i.e. A good quality product does what exactly user wants.
For a software product, the term quality refers to a product that is
  Functionally correct
  User friendly
Unlike hardware, the software products are used for longer duration as it keeps on changing to accommodate the new requirements.

## Slide 16: Quality Factors
The modern view of a quality associates with several quality factors for a software product.
  Correctness: A software product is correct only if it meets all the requirements specified in the SRS.
  Portability: the product must be able to work in different hardware and operating system environments.
  Usability: A software product is of good quality if all associated users can easily invoke the functionalities.
  Reusability: A quality software product must have the reusability attribute which makes the components of the product reusable in another scenario.
  Maintainability: A quality software product must be easy to maintain i.e., the error detection and correction could be done at ease.

## Slide 17: Quality Management System
A quality management system, simply known as quality system, is used by the organizations to ensure that the products they develop, have the desired quality.
A quality system usually involves following activities:
  Auditing of projects to check if the procedures are being followed.
  Collect, process and analyze metrics to check if the quality goals are being achieved.
  Review of the quality system to make it more effective
  Development of standards, procedures, and guidelines.
  Produce reports for the top management summarizing the effectiveness of quality system in the organization.
  Opting for “total quality management” that focuses on continuous process improvement rather than just quality control and quality assurance.

## Slide 18: Product Metrics vs Process Metrics
Product metrics help measure the characteristics of a product being developed. Ex: LOC and function point to measure size, metrics for effort, time, and cost estimation, etc.
Process metrics help measure how a process is performing. Ex: Review effectiveness, average error detection, average error correction, productivity, etc.

## Slide 19: ISO 9000
International Standards Organization, aka ISO, is a consortium of 63 countries established to formulate and foster the standardization.
ISO published its 9000 series of standards in 1987.
It serves as a reference between independent parties. It specifies the guidelines for maintaining a quality system.
It mainly address operational and organizational aspects.

## Slide 20: ISO 9000
ISO 9001
  This standard applies to the organizations engaged in design, development, production and servicing of goods.
  Applicable to most of the software industries
ISO 9002
  This series is applied to those organizations which do not design products but are only engaged in production.
  Ex: Mostly manufacturing companies
ISO 9003
  This is applied to the organizations that are engaged in installation and testing of products.

## Slide 21: Why ISO 9000 for software industry?
ISO 9000 is a generic standards that is applicable to a large section of industries.
Most of the ISO 9000 clauses are in generic terms which makes it difficult to apply in software industries due to several issues in software products.
Hence, ISO 9000 released a specific version, known as ISO 9000-3, in 1991 to categorically specify the standards for IT industry.
Following are the benefits of being an ISO 9000 certified company:
  Increased customer confidence
  Encouragement to software reusability
  Systematic, efficient and cost-effective development process.
  Deals with the weakness of the organizations.
  Sets the basic framework for the development of an optimal process and total quality management.

## Slide 22: How to get ISO 9000 certification???
Any organization, willing to get ISO 9000 certification, applies to ISO 9000 registrar for registration.
The ISO 9000 registration process consists of following stages:
  Application
  Pre assessment
  Document review and audit
  Compliance audit
  Registration
  Continued surveillance

## Slide 23: Important point for ISO 9000
ISO mandates that a certified organization can use the certificate for corporate advertisements only. They can't use the certificate to advertise their products.
  This is because ISO only certifies the production process, not the products.
In India, ISO 9000 certification is offered by BIS (Bureau of Indian Standards), STQC (Standardization, Testing, and Quality control) and IRQS (Indian registrar quality systems).
Shortcomings of ISO 9000
It does not guarantee a high-quality product as it only certifies the process.
ISO certification process is not full-proof, and no international accreditation agency exists.
ISO does not automatically lead to total quality management.

## Slide 24: SEI CMM
SEI Capability Maturity Model, SEI CMM, was proposed by software engineering institute of the Carnegie Melon University, USA.
It was originally developed to assist the US dept. of defence in software acquisition.
Gradually, many commercial organizations began to adopt CMM as a framework for their own internal improvement.
CMM is a reference model for inducting the software process maturity into different levels.
CMM is used in two ways: Capability evaluation and software process assessment.

## Slide 25: SEI CMM Levels
SEI CMM classifies the software companies into following maturity levels
  Level 1 (Initial)
    Very few or no defined and followed process
    Engineers follow their own process which results in chaotic development efforts
    Success of projects depend on individual effort and heroics. The successors face great difficulty in case if any individual leaves the company.
    Low quality products
  Level 2 (Repeatable)
    Basic project management practices are established.
    Necessary process discipline is in place to repeat the earlier success on projects with similar applications.

## Slide 26: SEI CMM Levels
Level 3 (Defined)
  The process for both management and development activities are defined and documented.
  Common understanding of activities, role, and responsibilities
  ISO 9000 aims at achieving this level
Level 4 (Managed)
  Focus is on software metrics like product metrics and process metrics
  Both process and product quality are measured to meet the specified quality requirements
Level 5 (optimizing)
  Process and product metrics are collected and analyzed for continuous process management
  Lessons learnt from past projects are incorporated into the process
  Continuous process improvement is the prime focus here.

## Slide 27: Key Process Area (KPA) in CMM
The Key Process Areas, KPA, of a level indicate the areas that an organization at the lower maturity level needs to focus to reach this level.
KPAs provide a way for an organization to gradually improve its quality of over several stages.
KPAs for each stage has been carefully designed such that one stage enhances the capability already built up.
  Trying to focus on some higher level KPAs without achieving the lower level KPAs would be counterproductive.

## Slide 28: ISO 9000 vs SEI CMM
ISO certification can be quoted in official documents whereas SEI CMM assessment is purely for internal purpose.
ISO certification is a generic standard. On the other hand, SEI CMM specifically applies to software companies.
ISO 9000 aims at SEI CMM level 3. SEI CMM does not require any ISO criteria.
ISO does not provide specific information for further improvement, whereas SEI CMM provides a list of key process areas for improvement.